## Slide 1: BEACON

## Slide 2
Bluetooth technology is a relatively short-range wireless communication technology, the main feature is low cost, replace the cable connection for the data network and a small peripheral interface to provide a unified connection.

## Slide 3
To monitor social distancing, a wearable node should be able to estimate its distance from the other nodes. This location awareness is enabled by a simple equation that relates the distance between the transmitter and receiver (d) to the received signal strength (RSS):
RSS=A-10nlog(d)
where A is the RSS at a distance of one meter and n is the signal propagation constant. The propagation constant depends on the environment and indicates how fast the strength of the received signal decreases with distance.
When a device is detected, the received information is analyzed to obtain its RSS. Based on this information, an approximate value for the distance is found and stored in RAM. The device can take several samples and store a programmable number of RSS and distance pairs for a given detected beacon.
the distance is compared with a threshold (2 m in this design). If it is below the threshold, the device generates an alert. Otherwise, it starts a new scanning cycle.

## Slide 4: Processeur
At the beginning, when the user login in the museum, the user take card BLU.
We will add all the information of the user in Cloud Database like user id.
In the Cloud Database, we are able to see the user's healthy history for all users.
If we found the user id healthy as COVID-19 positive, the BLU card triggers a real time alert (he or she not allow entering the museum.)
The museum have four Tablet Beacon.

## Slide 5: Processeur
When the Tablet Beacons are powered on, they periodically broadcast beacon messages over the advertising channel, just like ordinary beacon devices do.
BLU card discovers a beacon message from a certain Tablet Beacon.
Card BLU measures the RSS values and uses them to estimate how close it is to the neighboring BLU card. It is assumed to be in proximity when the distance is less than 2 m.
Card BLU triggers a real time alert to warn the user to keep a healthy distance from nearby users when it detects any physical distancing violation.
If there are ten messages or more in the Tablet Beacon (BLU card nearest to gather )the Tablet Beacons triggers a real time alert to warn the user to keep a healthy distance from nearby users when it detects any physical distancing violation.
All the generated signatures and observed signatures will be stored inside the user’s local storage.
Since the signature does not contain any information about the owner, there is no way for the user to trace or identify the original owner of the observed signatures. Furthermore, the signatures are deleted from the local storage permanently once it is expired.

## Slide 6
Yes
Yes
Start BLU
Reconnection
No Connection
Start Scanning
Device Detected
Store MAC In RAM
NO
Calculate the equation for Distant
Distant <2
Yes
Searching MAC on DB
MAC Found
MAC Number >10
Yes
NO
Play Sound in web view
Play Sound in web view
Play Sound in web view